## Slide 1: Case Study
MASCOT
Sally Forbes

## Slide 2: MASCOT
Electronic Exhibition In Rome 1962: https://www.britishpathe.com/video/electronic-exhibition-in-rome/query/3056_23
Remote handling system installing a tile in EFDA-JET’s new “ITER-Like Wall”: http://www.ccfe.ac.uk/videos.aspx?currVideo=4&currCateg=0

## Slide 3: The Robotic System
What hardware does it have?
  bilateral master / slave telerobotic manipulator system with haptic feedback
  attached to an articulated boom for positioning
What level of autonomy does it have?
  remotely controlled by an operator via control software (computer assisted tele-operation)
  software constraints on where arms can move, virtual forces / force scaling
  some semi-autonomous/ automatic moves (eg. arms move to “home position”)
What sort of software implements any autonomous functions?
  C++ on VX Works
Does the level of autonomy require hand-over between the system and a human operator
  yes

## Slide 4: The Task and Environment
What does the robotic system have to do?
  carry out inspection, maintenance, repair, removal and replacement of components inside the torus vessel during a shutdown
  wide range of in-vessel tasks including welding, cutting, bolting, handling and inspection
What materials is the robot handling/manipulating?
  tools required to carry out the above tasks
  activated metal components, beryllium tiles (20kg handling capacity)
Will the robot become activated (so, can we remove it from its environment for maintenance or replacement)?
  potentially contaminated with tritium and beryllium
  has to be bagged for movement to a contained facility after operation
Are there any other environmental constraints?
  only used in-vessel during a shutdown periods – vessel has become activated (gamma-rays) and is contaminated with tritium and beryllium dust
  do not want to contaminate torus vessel with fluids, polymers, or leave any debris, dropped materials

## Slide 5: Key Hazards
Hazards caused by and mitigated by the robotic system
  breach of vessel due to impact (eg. silica window)
  during combined manual and remote handling work in-vessel, potential for injury to operator and/or damage to pressurised suit
Hazards of the task
  personnel injury hazards on the master end
Hazards or challenges caused by the environment
  space constraints
  control systems remote due to radiation, large amount of wiring in the boom
  unknown conditions in the tours (erosion, deposition, movement of components)